Radar Parameters:

| Characteristics | Band 1 | Band2 |
| --- | --- | --- |
| RF Carrier Frequency (MHz) | 150 | 450 |
| RF Bandwidth (MHz) | 20 | 50 |
| Offset Video Band (MHz) | 20-40 | 5-55 |
| Transmit Pulse Width (usec) | 0.2-100 | 0.2-100 |
| PRF (kHz) | 0.001-10000 | 0.001-10000 |
| A/D Dynamic Range (dB) | 12-bit, 72 | 12-bit, 72 |
| Bytes per sample | 2 | 2 |
| Max. data rate to disk (Mbytes/sec) | 20 | 20 |
| Noise Figure (dB) | 4 | 4 |
| Sampling Frequency (MHz) | 120 | 120 |
| Peak Transmit Power | 200 W | 200 W |
| One-way System Loss (antenna and system | 2 dB | 2 dB |
| Antenna Peak Gain | 14 dB | Not available |
| Antenna Beam (4-elements) | 22 degrees – cross track | 22 degrees – cross track |
| System Response | Not available | Not available |
| Max Range Window |  |  |

Twin Otter Antenna Configuration:

The 4 existing antenna locations are at WS 154.09 (3.91m), WS 229.13
(5.82m), WS 290.66 (7.38m) and WS 353.66 (8.98m) of each wing.  These actual
locations are different than the locations listed in the diagram.

P-3 Antenna Configuration:

The elements in each array are spaced 1 meter apart and 50 cm below the wing.  The center of the array is ? m (determining exact dimension) from the centerline of the aircraft.